## Slide 1
🧠➜🖥️➜🌐
Powering AI: The Hardware Infrastructure Story
How "Nova", a first enterprise AI assistant, grows from one server to a real platform
For presales & sales teams · 2-hour session
Notes: Set the frame: every component is introduced only when our story needs it. Ask who has heard GPU, endpoint, RAG.

## Slide 2
1 · THE NEED
Meet Northwind Finance
🧑‍💼
Sales reps need answers fast
➜
📚
Answers buried in 10,000 docs
➜
⏳
Hours lost every week
➜
💡
Idea: an AI assistant called Nova
Nova is our running example for the whole session.
Notes: Relatable pain: nobody starts with hardware, they start with a business need. Nova drives every infra decision.

## Slide 3
ROADMAP
Our journey: add a part only when Nova needs it
🧩
Stack
⚙️
Compute
💾
Storage
🔌
Network
🚪
Serving
🔄
Data flow
🛡️
Security
🔎
One request
Notes: Preview. We open with the need and close by following one real request through everything.

## Slide 4
2 · THE STACK
The AI stack: 8 layers, top to bottom
Users & apps
Chat, CRM, email
Orchestration / RAG / agents
Adds context and tools
Model
The trained 'brain' (weights)
Serving runtime
vLLM, Triton: runs the model
Compute
CPU · GPU · TPU
Storage
Docs, vectors, weights
Network
Connects everything
Facility
Power, cooling, cloud or on-prem
Notes: The single most useful picture. Customer questions always map to one layer. The model sits in the middle: software above, hardware below.

## Slide 5
2 · THE STACK
Where does the model live?
📦
Model = big files of weights (GBs to 100s of GB)
➜
💾
Stored on disk or object storage
➜
🚀
Loaded into GPU memory at startup
➜
💬
Answers requests via an endpoint
Sizing rule #1: the model must fit in GPU memory.
Notes: Demystify: a model is just files. The hardware question is where those files run fast enough.

## Slide 6
2 · THE STACK
Training vs inference: build vs use
🏋️
Training
Builds the model. Weeks, thousands of GPUs. Mostly labs and vendors.
🎛️
Fine-tuning
Adapts a model to your data. Hours to days, a few GPUs.
💬
Inference
Uses the model 24x7. Latency matters. Where most enterprises spend.
Notes: Nova is inference only. Most customer conversations are about inference sizing.

## Slide 7
3 · COMPUTE
CPU: the versatile manager
🧠
Few powerful cores
Roughly 8 to 128 cores, handles varied logic
🔧
Nova uses it for
Web app, APIs, data prep, small models
🐢
Limit
Too slow for big-model math
Notes: CPUs are not going away: they orchestrate, pre-process and serve the surrounding app.

## Slide 8
3 · COMPUTE
GPU: thousands of small workers
CPU: a few big cores
GPU: thousands of small cores
AI is mostly matrix math, which can be split across many workers at once.
Notes: Analogy: CPU is 8 expert chefs, GPU is 1,000 line cooks doing the same chop. AI math is exactly that repetitive.

## Slide 9
3 · COMPUTE
TPU and other accelerators
🔷
TPU
Google's AI chip, used via Google Cloud
🟠
Custom ASICs
e.g. AWS Trainium and Inferentia, efficient per task
🟣
NPU / edge
AI inside laptops, phones, cameras
🟢
GPU vendors
NVIDIA leads; AMD and Intel are growing
Notes: GPUs are the default, but specialised chips can lower cost or power. Software ecosystem is the real lock-in.

## Slide 10
3 · COMPUTE
Choosing the engine (illustrative)
Chart: 
| CPU: flexibility | CPU: AI throughput | GPU: AI throughput | GPU: flexibility | TPU/ASIC: AI efficiency
v | 90 | 10 | 95 | 60 | 90
Relative sketch, not a benchmark.
Notes: Do not quote numbers from this slide; it shows shape only.

## Slide 11
3 · COMPUTE
Memory decides which model fits (GB, FP16)
Chart: 
| 7B model | 13B model | 70B model | 405B model
v | 14 | 26 | 140 | 810
4-bit quantization shrinks weights roughly 4x; add room for the KV cache.
Notes: FP16 is 2 bytes per parameter. One 80 GB GPU cannot hold 70B in FP16, so you need several GPUs or quantization.

## Slide 12
STORY · NOVA V1
Launch: one GPU server, small model
📄
500 docs
➜
🤖
7–8B model
➜
🖥️
1 GPU server
➜
👥
20 pilot users
Low cost, fast learning. Enough to prove value.
Notes: Encourage customers to start small. A pilot proves value before big capex.

## Slide 13
3 · COMPUTE
Where to run it: 4 deployment options
☁️
Cloud API
Fastest start, pay per use, data leaves your walls
🏗️
Cloud GPUs
Rent VMs, you control the model
🏢
On-prem
Own GPUs, data stays, upfront cost
🔀
Hybrid
Sensitive on-prem, burst to cloud
Notes: Driven by data sensitivity, cost profile and skills. Regulated customers often land on hybrid.

## Slide 14
3 · COMPUTE
Packaging: containers and Kubernetes
📦
Container bundles model + runtime
➜
☸️
Kubernetes places it on GPU nodes
➜
📈
Scales up and down, self-heals
Same package runs on cloud or on-prem.
Notes: Containers give portability; Kubernetes gives scheduling and recovery. Needed beyond one server.

## Slide 15
4 · STORAGE
Nova needs memory: storage tiers
Hot: local NVMe SSD
Model weights, caches, fastest
Warm: NAS / SAN / block
Shared files, databases
Cold: object storage
Docs, backups, data lake: cheap and huge
Special: vector database
Embeddings for semantic search
Notes: Faster costs more. Weights hot, source docs cold, embeddings in a vector DB.

## Slide 16
4 · STORAGE
Storage options at a glance
⚡
Local NVMe
Lowest latency, fast model load, not shared
🗂️
NAS (NFS/SMB)
Shared files, simple, moderate speed
🧱
SAN / block
Databases, low latency, enterprise HA
🪣
Object (S3-style)
Scale and cost, source of RAG documents
🏎️
Parallel file system
Many GPUs read at once, mainly training
Notes: For inference, NVMe plus object storage covers most cases. Parallel file systems show up in training clusters.

## Slide 17
5 · NETWORK
Three networks, three jobs
🔗
Inside a server: NVLink, PCIe (GPU to GPU)
🕸️
Between servers: InfiniBand, RoCE Ethernet
🌐
To users: LAN/WAN, VPN, load balancers
Notes: Different bottlenecks at each level. Many AI slowdowns are network, not GPU.

## Slide 18
5 · NETWORK
Network options
🔌
Ethernet 25–100G
Enough for inference and storage traffic
🚄
Ethernet 400G+ with RoCE
AI clusters; needs lossless tuning
⚡
InfiniBand
Lowest latency, large training
🧬
NVLink / NVSwitch
GPUs behave like one big GPU
Small-model inference: standard Ethernet. Training clusters: network is the bottleneck.
Notes: Inference rarely needs exotic fabrics; multi-node training does.

## Slide 19
STORY · SCALE
Nova goes viral: 20 users become 2,000
📣
Word spreads
➜
🐌
Slow answers, timeouts
➜
⚖️
Add load balancer + more GPU replicas
➜
✅
Steady response times
Notes: Trigger for the next components: concurrency, not model quality, forces scale-out.

## Slide 20
6 · SERVING
Traffic path: gateway and load balancer
👥
Users
➜
🚪
API gateway: auth, limits
➜
⚖️
Load balancer
➜
🖥️
GPU replicas A · B · C
Health checks remove a failing replica automatically.
Notes: Load balancers spread requests; gateways add identity and quotas. Two different jobs, often confused.

## Slide 21
6 · SERVING
Model endpoint: the front door
🔌
One stable URL
Apps call /chat; the model behind can change
🔐
Auth and quotas
Keys, SSO, per-team limits
🧪
Versioning
Blue/green upgrades, A/B tests
Notes: Endpoint = how applications consume the model. Cloud APIs give one out of the box; on-prem you build it.

## Slide 22
6 · SERVING
Serving runtime: squeezing the GPU
⚙️
Inference server
vLLM, Triton, TGI load and run the model
🧺
Batching
Serve many users per GPU pass
🧠
KV cache
Remembers context, eats GPU memory
📊
Autoscaling
Add replicas when queue grows
Notes: This is where cost per answer is won or lost.

## Slide 23
7 · DATA FLOW
Nova learns your data: enterprise data flow (RAG)
📚
Docs, CRM, wiki
➜
✂️
Chunk + embed
➜
🗃️
Vector DB
➜
🔎
Retrieve top matches
➜
🤖
LLM answers with sources
The model stays general; your knowledge stays in your data layer.
Notes: RAG avoids retraining. It touches storage, network and compute, which drives infra sizing.

## Slide 24
CHECK
Are you missing something? Checklist
⚖️
Load balancer
Spread traffic
🚪
API gateway
Auth, limits
🗃️
Vector DB
Semantic search
⚡
Cache
Cheaper repeat answers
📈
Observability
Latency, GPU use, cost
🪪
Identity
SSO, roles
🛑
Guardrails
Block unsafe or leaky output
🔁
HA and DR
Failover, backups
Notes: Also mention power, cooling, rack space and FinOps (cost tracking); they often decide on-prem feasibility.

## Slide 25
8 · SECURITY
Security touches every layer
Apps and agents
Prompt injection, tool permissions
RAG and data
Access-aware retrieval, no leaks
Model
Untrusted weights, licensing
API / endpoint
AuthN/Z, rate limits, logging
Infrastructure
Segmentation, encryption, GPU tenancy
Notes: Two lenses: security for AI (protect the AI system) and security of AI outputs. Keep it high level.

## Slide 26
TOOLKIT
Presales cheat-sheet: questions to ask
👥
How many users, at peak?
🧠
Open model or vendor API?
📚
How much data, and where?
⏱️
What latency is acceptable?
🏢
Cloud, on-prem or hybrid? Compliance?
💰
Budget, power and cooling limits?
Notes: Those six questions size most AI infra deals. Suggest role-play in the session.

## Slide 27
FINALE
One request, end to end
1️⃣💬
Rep asks Nova
➜
2️⃣🚪
Gateway checks identity
➜
3️⃣⚖️
Load balancer picks a replica
4️⃣🗃️
RAG fetches docs from vector DB
➜
5️⃣🖥️
GPU generates the answer
➜
6️⃣🛡️
Guardrails check, answer returns
Notes: Walk slowly and tie each step back to earlier slides: storage, network, compute, serving, security.

## Slide 28
RECAP
Key takeaways
🧩
Model sits between apps and compute
⚙️
GPUs for AI, CPUs orchestrate, ASICs specialise
💾
Storage and network are silent bottlenecks
🚪
Endpoints, LBs and gateways make it enterprise-ready
🔄
Data flow and security make it trusted
Notes: Close on the story: Nova grew because each layer answered a real need.